## VCB-3424		Architect & Engineer Specification

### Bid Spec

- Description

The black and white video camera described shall be a Sanyo Model number VCB-3424 or equivalent. The Camera described shall be an industrial grade high sensitivity black and white video camera.

- Bid Specifications

The black and white video camera shall incorporate an interline transfer method 1/3” charge coupled device (CCD) with approx. 270,000 picture elements (542Hx492V). This camera shall produce a picture with more than 400 lines of resolution and have a minimum light requirement of 0.07 lux with F1.2 lens and a S/N ratio of more than 50dB. The video output level shall be 1.0Vp-p (75 ohms, composite) with a BNC type connection.

The camera shall be C-mount and CS-mount selectable with a C mount adapter (included). The camera shall include (1) mounting bracket (1/4”-20UNC) which can be mounted either on the top or the bottom of the camera. The video camera shall have an auto iris connector on the side of the camera body to permit connection of DC: iris control coil only type lenses (galvanometric iris without amplifier type) and VIDEO: DC power and video signal supply auto-iris type lenses (with amplifier type) type lenses.

The video camera shall have an available Backlight compensation circuit, Electronic/Auto Iris and Flange back adjustment. The video camera shall have a mirror effect feature for reverse angle viewing.

The camera shall not exceed a dimension of 2.2” x 1.77” x 3.92” (56x45x99.5mm)(w/o lens mount and camera mount) and weigh no more than 330 grams. Power requirements for the video camera shall be 24V ((4V), 60Hz, 1.4W min (w/o Auto Iris lens).  The video camera shall have an LED type indicator to indicate the presence of power. The video camera shall be constructed of a durable metal cabinet and shall be magnetic and electrostatically shielded. The camera shall feature solid state components to resist shock and vibration. The video camera shall be ISO9001 certified and UL listed.

- Minimum Performance Specifications

| Specifications |  |
| --- | --- |
| model | VCB-3424 |
| Scanning system | EIA Standard:525 lines, 30 frames/sec |
| Image device | Interline transfer method CCD |
| Image size | 1/3” (Approx. 4.8mm x 3.6mm) |
| Picture element | 542(H)x492(V):All picture elements 512(H)x492(V):Effective picture elements |
| Optical blank element | Horizontal 2:in front, 28:in back |
| Unit (pixel) cell size | 9.6(H) x 7.5(V) (m |
| Geometry | No geometric distortion |
| Synchronizing system | Line lock |
| Interlace | PLL2:1 interlace |
| Resolution | Horizontal 400 TV lines Vertical 350 TV lines |
| Video output level | 1.0Vp-p(75(, composite) |
| Video S/N ratio | More than 50dB |
| Minimum Illumination | Scene: 0.1 lux(F1.4 lens), 0.07 lux(F1.2 lens) Imager: 0.01 lux |
| Gamma correction | 0.45 fixed |
| Backlight compensation | ON/OFF, Manual switching, center zone light measuring system (activates when used with auto-iris lens) |
| Lens mount | CS mount (C mount: Using C-mount adapter supplied) |
| Flange back adjustment | 12.5mm –0.8 to +0.8mm |
| Camera mount | ¼” – 20 UNC x 2 (Top/Bottom) |
| Control | V Phase adjustment LINE PHASE VR Rear Lens Iris level LEVEL:L,H VR Side Electronic Iris E.I.:ON/OFF SLIDE SW Side Backlight ON/OFF SLIDE SW Side |
| Sockets | Video VIDEO OUT BNC Lens LENS OUT 4-pin Power Supply 24V AC, GND 3-pin terminal |
| Electronic Iris Range | 0.07 lux to 42,000 lux (F1.2 lens) 0.1 lux to 57,000 lux (F1.4 lens) 0.4 lux to 228,000 lux (F2.8 lens) |
| Light control | Electronic iris (indoor use) or optional auto iris lens |
| Auto iris output and connection | DC: iris control coil only type lens (Galvanometric iris without amplifier type) Drive Coil (+-), Brake Coil (+-), Ground Socket Pin No.1 Brake Coil- Socket Pin No.2 Brake Coil+ Socket Pin No.3 Drive Coil+ Socket Pin No.4 Drive Coil- VIDEO:DC Power and Video signal supply auto-iris type lens (with amplifier type) +12V DC (MAX 50mA), Video(High impedance), Ground Socket Pin No.1 +12V DC (50mA max) Socket Pin No.2 Not Used Socket Pin No.3 Video Out(1Vp-p Hi impedance Socket Pin No.4 GND (Video signal and DC) |
| Environmental Conditions | Operating: Temperature: 14( to 122(F Humidity: Within 90% relative humidity Storage: Temperature -4( to 158(F Humidity Within 70% relative humidity |
| Power Indicator | LED |
| Power Requirement | 24V AC (-4 to +4V), 60Hz |
| Power consumption | 1.4W (w/o auto iris lens) |
| Size (WxHxD) | 56x45x99.5mm (2.2”x1.77”x3.92”) (w/o lens mount and camera mount) |
| Weight | .73lb (330g) |

*Note all non-metric specifications are approximate.

http://www.securitex.com.sg